## Slide 1
June 26th, 2026
Products Trading
Products Trading
Refinery Outages
2027 Outlook by Unit
Capacity offline by unit, region & operator, and what it tightens
2027: ExxonMobil full-year (verified vs their plan); all other operators H1-confirmed only
PROPRIETARY

## Slide 2
Total 2027 Outages by Unit, and What They Tighten
Capacity offline by unit & month; solid = confirmed, hatched = non-Exxon H2 (not yet booked)
Products Trading
1
Key takeaways:
CDU down cuts the whole site's run, every product. FCC = gasoline + octane. Reformer = octane. Hydrocracker = diesel/jet.
Confirmed peak (all H1): CDU ~1,063, FCC ~492, hydrocracker ~219, reformer ~206 kbd.
Units read separately, never added: a 250 CDU plus a 100 FCC is not '350 offline'.
Solid = confirmed (Exxon full-year + everyone's H1). Hatched = non-Exxon H2: don't trade the autumn spike as real.
Day-weighted offline (a unit down part of a month counts only its days down), each unit once per month. Non-Exxon H2 2027 is a floor that fills in.

## Slide 3
What's Driving the Numbers: the Biggest Outages
Each bar is one unit's nameplate offline (kbd) in 2027, colored by PADD (region)
Products Trading
2
Key takeaways:
Big tonnage sits in PADD 3: that's where one outage moves USGC supply and the export barrel most.
Biggest: Garyville (275 kbd), Cherry Point (250 kbd), Joliet (250 kbd). Mostly crude (CDU); one CDU down cuts the whole site's run.
Read each bar alone: individual units, never added. Biggest single outage ~275 kbd, not a summed total.
Hatched = non-Exxon H2: still being booked, an indicative floor, not confirmed.
Per-unit nameplate offline, the 12 biggest focus-unit outages of 2027. Color = PADD region; hatched = non-Exxon H2 (indicative).

## Slide 4
H1 Planned Outages per Unit & Month: 2025 / 2026 / 2027
Like-for-like Jan-Jun planned offline, by unit and month (2027 confirmed through H1)
Products Trading
3
Key takeaways:
H1 is the only honest cross-year read: 2027 is booked through June; H2 is still being scheduled.
2027 runs heavier than 2025 and 2026 in most H1 months: the orange bar stands tallest.
Crude (CDU) averages ~548 kbd vs ~325 (2026), ~393 (2025); crests in Mar (~1,063 kbd).
Heavier spring = tighter product supply. Read each unit and month on its own, never added.
Day-weighted capacity offline by month, planned only, each unit once per month. Per-panel y-axis. 2025/26 actuals; 2027 the booked plan.

## Slide 5
Outages by PADD by Unit: Where It Tightens
2027 crude (CDU, top) and cat-cracker (FCC, bottom) offline by region & month
Products Trading
4
Key takeaways:
PADD 3 (Gulf) is the swing region: most crude and FCC work lands there, tightening USGC supply and the export barrel.
PADD 2 (Midwest) carries the spring crude (Joliet). PADD 5 (West) is islanded: a California outage isn't bailed out by other regions.
Windows are spring (Mar-May) and autumn (Sep-Oct); summer is protected for driving-season gasoline.
Past the dotted line (H2) is non-Exxon, unconfirmed: those autumn bars are a floor that grows as operators book.
Day-weighted concurrent capacity offline by month, stacked by PADD. P1 NE, P2 Midwest, P3 Gulf, P4 Rockies, P5 West.

## Slide 6
ExxonMobil 2027 by Unit
Each unit's turnaround as its own bar, nameplate capacity offline (kbd)
Products Trading
5
Key takeaways:
ExxonMobil is the only operator with a full-year 2027 plan, so its H2 is the only confirmed H2. Everyone else is H1-only.
Per unit, never summed: the 'Exxon ~700 kbd' figure was 8 Joliet units in one April turnaround added together. It's really ~250 kbd of crude.
Reconciled to Exxon's own corporate plan (7 units): Baytown & Beaumont FCC in Q1, Joliet crude Apr-May, Baton Rouge crude in autumn.
Cross-checked against ExxonMobil's corporate turnaround plan; match = same refinery + unit class, overlapping months.

## Slide 7
2027 Unplanned Scenario: the Risk on Top of Planned
Potential unplanned offline (kbd) modeled on the 2023-26 seasonal pattern
Products Trading
6
Key takeaways:
2027 has no actual unplanned yet: this is the risk range on top of the booked plan.
Average ~13,046 kbd unplanned; Conservative ~10,437 (calm year), Active ~16,959 (heavy). Booked planned is ~15,691 kbd.
Implied total ~26,127 / ~28,737 / ~32,650 kbd (Conservative / Average / Active).
Risk peaks in Feb (winter freeze) and Sep-Oct (turnaround overlap); summer is the trough.
Trade it: Active = stress case for supply tightness; Conservative = the floor.
Scenario = mean 2023-26 monthly unplanned shape (completeness-aware) x {0.8 / 1.0 / 1.3}. A risk range, not a forecast.